## Slide 1: Sensors, instruments and Experimentation
Introduction by Ashok Ranade

## Slide 2: Syllabus
Introduction to construction and characteristics of sensors. Experiments involving application of sensors for physical quantities like temperature, pressure, force, torque, strain, velocity, acceleration, linear and angular speed and displacement, volumetric and mass flow rates, illumination, and sound level etc. Introduction to calibration of sensors and data acquisition system
Basic Mechanical measuring instruments: Vernier caliper: Micrometer: Coordinate Measuring Machine: Pressure gauge :

## Slide 3: Books
Principles and applications of Electrical
Engineering
Fifth Edition
By Giorgio Rizzoni
McGraw-Hill (India)
References on the net

## Slide 4: Examination scheme
Quiz 1 : 11%
Mid term test: 22%
Quiz 2 : 6%
Assignments : 11%
Project: 15%
End term Examination : 35%
All examinations open book and on LMS

## Slide 5: Grade Rubric
Grades | A | A- | B+ | B | B- | C+ | C | D | NP
Marks Range | 90-100 | 80-89 | 70-79 | 60-69 | 50-59 | 40-49 | 35-39 | 30-34 | 0-29
Absolute grading

## Slide 6: Measurement and control systems
Engineering applications require measurement and control of physical quantities
Satellite communication
Antenna position

## Slide 7: Robot position

## Slide 8: Other Examples
Measurement and control of temperature of oven
Measurement and control of Flow in flood control

## Slide 9: Transducers
Capable of converting one physical quantity into another type of physical quantity
The device which converts a non-electrical quantity into an electric quantity is called a sensor
Examples
Thermocouple
Microphone
The device which converts an electrical quantity into a non electrical quantity is called actuator
Heater
Speaker

## Slide 10: An application
Temperature alarm
Temperature
Sensor
Comparator
Vr

## Slide 11: One more application
Speed and acceleration measurement
Speed sensor
A to D converter
Processor
Speed
38 RPM
Acceleration
4 m/sec2

## Slide 12: Input output characteristics of a sensor
Manufacturers specify the sensor characteristics
x is the input
y is the output
y = f(x)

## Slide 13: Sensor calibration
Source to vary
The input quantity
Sensor
Accurate Meter for output quantity
Accurate meter for input quantity
x
y
If non linear manufacturer will also provide polynomial equation
often a graph is provided by the manufacturer
If approximately linear, best fit line is given.
i.e. compressor
Heating element

## Slide 14: Curve fitting
This is the process of finding a suitable equation between y and x when table of values of x and y is known.
Often a polynomial is found
The curve fitting will give the values of constants a0,a1 etc
Other equations are also possible
Many programming languages have the function for curve fitting
Excel also has the facility

## Slide 20: Class Exercise 1
Let x vary from 0 to 1 with increment of 0.1
Let y = x3
In Excel calculate y for each value of x and find
the polynomial for y in terms of x. It will be close to x3.
Calculate y using the polynomial and compare with original values

## Slide 21: Solution to Exercise 1

## Slide 22: Class Exercise 2
Let x vary from 0 to 1 with increment of 0.1
Let
In Excel calculate y for each value of x and find
the polynomial for y in terms of x. Calculate y using the polynomial and compare with original values.
Experiment with two or more trend-lines for more accurate results

## Slide 23: Solution to Exercise 2

## Slide 24: More error with single trendline

## Slide 25: Sensors instruments and experimentation
By Ashok Ranade
02 Some aspects of instrument design and errors in measurements

## Slide 26: Analog Instrument
Suppose we want to build an analog temperature measuring instrument with range of 0 to 100 degree C, using a given sensor and a voltmeter
Sensor characteristics are 10mV/degree centigrade
Voltmeter is 0 to 5 volts.
Output of sensor is 1 volt at 100 degrees so for full scale deflection the amplifier with gain 5 is required
T
Sensor
Amplifier
Gain 5
Voltmeter
V
Vo
V= 0.01 T
Vo = 0.05T

## Slide 27: Calibrating the meter
Vo = 0.05T
T= Vo/0.05
Vo | T
0 | 0
1 | 20
2 | 40
3 | 60
4 | 80
5 | 100

## Slide 28: Linear and non linear
Chart: 
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
y1(mV) | 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000
y2(mV) | 0 | 10 | 40 | 90 | 160 | 250 | 360 | 490 | 640 | 810 | 1000
x Temp | y1(mV) | y2(mV)
0 | 0 | 0
10 | 100 | 10
20 | 200 | 40
30 | 300 | 90
40 | 400 | 160
50 | 500 | 250
60 | 600 | 360
70 | 700 | 490
80 | 800 | 640
90 | 900 | 810
100 | 1000 | 1000
Temperature in degrees Centigrade
Output in mV
Scale is crowded at low temperatures for non linear sensor for analog display

## Slide 29: Digital Instrument
Sensor
A to D converter
Processor
Display
Easy calculation for linear sensor
Difficult calculation for non-linear sensor
Table look up can be used instead of solving the equation. Will need memory.
In general

## Slide 30: Algorithm for the Digital instrument
(1) Read y1
(2) calculate x = f-1(y1) or get x from look up table
(3) Send to display
(4) Delay
(5) Go to (1)

## Slide 31: Class Exercise 2.1
A force sensor has input output characteristics given
by
Where V is the output voltage and F is the force in
Newtons
We wish to build an analog Force meter which uses a voltmeter of the range 0-10 volts. The calibration should be valid for the force range from 0 to 10 Newtons. (Full scale). So in your block diagram you have Force sensor and 0 – 10 dc voltmeter. What else you need? Think and design the complete block diagram for the meter . Show the calibration so that you get one decimal digit accuracy.

## Slide 32: Solution to Exercise 2.1
We have
So when F = 10 Newtons
V = 6.324555 volts
Clearly we can not get full scale deflection if we connect the output of sensor to the voltmeter. So we need an amplifier with gain = 10/6.324555
= 1.581139

## Slide 33: Block diagram
Force
sensor
Amplifier
F
Vo

## Slide 34: Calibration
F | V | Vo
0 | 0 | 0
0.1 | 0.632 | 1
0.5 | 1.414 | 2.2
1 | 2 | 3.2
2 | 2.828 | 4.5
3 | 3.464 | 5.5
4 | 4 | 6.3
5 | 4.472 | 7.1
6 | 4.899 | 7.7
7 | 5.292 | 8.4
8 | 5.657 | 8.9
9 | 6 | 9.5
10 | 6.325 | 10
0
.1
.5
1
2
3
4
5
6
7
8
9
10

## Slide 35: Exercise 2.2
Consider the block diagram below
Sensor
x
Attenuator
A to D
Converter
Processor
Display x
y
y1
y2
x | Y(Volts)
0 | 15
3 | 2
8 bit A to D converter is used and range of input voltage to ADC is 0 to 5 volts. Obtain the expression for x in terms of y2 that processor will use

## Slide 36: Solution to Exercise 2.2
Since ADC accepts the maximum input of 5 volts y1 = y/3
Since ADC is 8 bit its output ranges from 0 to 255. And 255 corresponds to y1 = 5. Also ADC is linear so
Substituting for y1 and rearranging we get the final answer

## Slide 37: Error in measurements
What is Error ?
Difference between measured and true value
usually in % of full scale reading
Accuracy
Conformity of the measurement to the true value

## Slide 38: What is a true value ?
As measured by an instrument without error
This does not exist
However highly accurate instruments called Primary standards are available
These are available in International and National laboratories
Less accurate instruments are calibrated using Primary standards
These are secondary standards more often used
Working standards
These are calibrated using secondary standards

## Slide 39: Calibration procedure
Source with regulator to control
the quantity under test
Heat source
Compressor
Voltage source
Instrument under test
Secondary or working standard

## Slide 40: Types of Measurement errors
Two types of errors
Systematic errors
Due to instrument inaccuracies
Faulty design of an experiment
Repeatable
Random errors
Human errors
Noise
Not repeatable

## Slide 41: Error distributions (Magnitude)
True value
Measured values
Systematic errors (Magnitude measurement)
True value
Measured values
Random Errors

## Slide 42: Error distribution (Magnitude and phase)
True value
Measured values
Systematic errors
Magnitude
Phase

## Slide 43: Error distribution (Magnitude and phase)
True value
Measured values
Random errors
Magnitude
Phase

## Slide 44: Average of many readings
We will take two examples
(1) An object is to be weighed. Then to get better
accuracy , it will be weighed many times. Let us
say the readings are W1, W2, --- Wn. And we
will take average of these readings

## Slide 45: Measuring input-Output Characteristics
(2) We wish to find input – Output characteristics of
a device (i.e. Sensor).
Let us say input is denoted by x and output is
denoted by y. There is a regulator to set
x and we adjust the regulator to set x from x1 to xn
and measure corresponding y1 to yn values. However for better accuracy , each regulator setting is repeated for , say, nx times and average of each x and y value is taken.

## Slide 46: Average of many measurements
Many values of the variable, say x , are measured
Similar equations apply for y values

## Slide 47: Standard Error
Standard error measures how much discrepancy is likely to be in the sample mean and the population mean.
Standard deviation measures dispersion of the data set relative to its mean.

## Slide 48: Standard error formula
It is expected to depend on SD and n. Larger the n closer will be the mean to the true value.

## Slide 49: Drill Exercise 2.2
An object is weighed 7 times. The measured values are shown below. Clearly there are errors. Find the mean value of the weight and the standard error using Excel
Object weight(in KG)
9.9
10.1
10.4
9.8
9.7
10
9.6

## Slide 50: Answers
Object weight(in KG)
9.9
10.1
10.4
9.8
9.7
10
9.6
Mean | 9.929
Std Dev | 0.269
Std Dev (n-1) | 0.291
Std Error | 0.11

## Slide 51: Accuracy and precision
Precision
degree of reproducibility of a measurement.
More accurate, Less precise
Less accurate, more precise
Target location in GPS

## Slide 52: Resolution
Smallest measurable increment
A voltmeter capable of measuring minimum value of 1mV has more resolution than the one capable measuring minimum value of 10 mV considering same full scale value for both.

## Slide 53: Span and range
Span : Linear operating range
A temperature transducer may have a linear relation between temperature and output voltage over a temperature range of 0 to 150 degrees centigrade
Range : The range of measurable values
Linearity : Conformity to an ideal linear calibration

## Slide 54: Non-linearity
Deviation from the linearity over a specified range

## Slide 55: Best fit line
A practical sensor will have some non-linearity
Manufacturers specify the best fit line
Linearization of sensor
Data pairs (x1,y1), (x2,y2),(x3,y3),---(xn,yn)
Least square method
y = mx + b

## Slide 56: An Example
x | y
0 | 0
1 | 2.5
2 | 3.2
3 | 5.4
4 | 8.5
5 | 9.8
6 | 12.5
7 | 13.4
8 | 16.3
9 | 17.5
10 | 20.4
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
y | 0 | 2.5 | 3.2 | 5.4 | 8.5 | 9.8 | 12.5 | 13.4 | 16.3 | 17.5 | 20.4

## Slide 57: The best fit line
x | y | z
0 | 0 | -0.105
1 | 2.5 | 1.907
2 | 3.2 | 3.919
3 | 5.4 | 5.931
4 | 8.5 | 7.943
5 | 9.8 | 9.955
6 | 12.5 | 11.97
7 | 13.4 | 13.98
8 | 16.3 | 15.99
9 | 17.5 | 18
10 | 20.4 | 20.01
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
z | -0.10455 | 1.9073 | 3.9191 | 5.9309 | 7.9427 | 9.9545 | 11.9664 | 13.9782 | 15.99 | 18.0018 | 20.0136

## Slide 58: Worst case
x Input
y Output
Fitted
Max Deviation = Max | ymi – yfi| : i = 1 to n
ym is y measured and yf is y fitted

## Slide 59: Most likely deviation
n-2 is used due to two reasons
Measured values are mean of samples and not true values
Two variables are involved in measurement , x and y

## Slide 60: Sensors, Instruments and Experimentation
By Ashok Ranade
03 Computerized measurement and control systems

## Slide 61
Sensor 1
Analog input
Sensor 2
Output device1
Computer Board
Analog output
Digital Output
BLOCK DIAGRAM
44.2
Analog Input

## Slide 62: Development of software
Software written on a general purpose computer
Uploaded on the control board
After this the control board can be used as a stand alone board for some application

## Slide 63
USB
Connector
Battery Connector

## Slide 64: Input/Output Pins
Analog Input (6 pins)
Any value between Vmin to Vmax
For Arduino : 0 to 5 volts
Digital pins (14)
Digital Input : 0 or 5 volts
Digital Output : 0 or 5 volts
PWM output (6)
Analog output

## Slide 65: Analog to digital converter
Computer uses numbers in binary form
A/D converter converts analog input into a multibit binary number
In Arduino it is 10 bit number
So 0 volts Corresponds to binary 0000000000
decimal 0
5 volts correspond to binary 1111111111
decimal 1023

## Slide 66: Sampling rate of ADC in Arduino
Sampling rate = 9650 samples/Sec
Maximum theoretical frequency of the input analog signal is half of this
Other rates are also possible with advanced programming

## Slide 67: PWM waveform
Tw
T
t
v
5

## Slide 68: Control of duty cycle
PWM : Duty cycle
0% for 00000000 (Decimal 0)
100 % for 11111111 (Decimal 255)

## Slide 69: Program structure
Declarations

## Slide 70: Program 1(Blinking LED)
Write a program to blink the LED. Turn it on for 1 second and turn it off for 1 second.

## Slide 71: Program 1

## Slide 72: Tinkercad Demo

## Slide 73: Class Exercise 3.1 3 Bit D to A converter
V1 | V2 | V3 | Vo
0 | 0 | 0 | 0
0 | 0 | V | V/8
0 | V | 0 | V/4
0 | V | V | 3V/8
V | 0 | 0 | V/2
V | 0 | V | 5V/8
V | V | 0 | 6V/8
V | V | V | 7V/8
Build in Tinkercad and test. Chose R = 1Kohms
(Other values are also possible). Use three slide switches to give digital inputs. Use a multimeter to measure the output and verify the table

## Slide 74: Solution follows

## Slide 75: All inputs zero
V1=0
V2=0
V3=0

## Slide 76: Input 00V
V1=0
V2=0
V3=5
Vo = V/8 = 5/8 = 0.625 volts= 625 mVolts

## Slide 77: Input 0V0
V1=0
V2=5
V3=0
Vo = V/4 = 5/4 = 1.25 volts

## Slide 78: Input V00
V1=5
V2=0
V3=0
Vo = V/2 = 5/2 = 2.5 volts

## Slide 79: Sensors, Instruments and Experimentation
By Ashok Ranade
04 Arduino exercises

## Slide 80: Digital Read function
Syntax
digitalRead(pin)
Description
Reads the value from a specified digital pin,
either HIGH or LOW.
x = digitalRead(Inpin)

## Slide 81: Class Exercise 4.1
Write a program to sense a slide switch. If it is connected to +5 , led connected to pin 12 flashes periodically. Otherwise the led remains off.

## Slide 82: Tinkercad simulator

## Slide 83: Analog Read and Serial Communication
analogRead(potPin)
x = analogRead(potPin);
x ranges from 0 to 1023
This will read the analog voltage from the input pin
Serial.begin(9600)
This will establish serial communication between
computer monitor and Arduino. This is in the set up
section.
Serial.println("ADC output");
Serial.println(x);

## Slide 84: Digital to Analog Conversion calculation
Digital Value | Analog Value
0 | 0
100 | 0.488758553
200 | 0.977517107
300 | 1.46627566
400 | 1.955034213
500 | 2.443792766
600 | 2.93255132
700 | 3.421309873
800 | 3.910068426
900 | 4.398826979
1023 | 5
Chart: Digital to analog conversion
| 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1023
 | 0 | 0.48876 | 0.97752 | 1.4663 | 1.955 | 2.4438 | 2.9326 | 3.4213 | 3.9101 | 4.3988 | 5

## Slide 85: An Exercise 4.2
A potentiometer is used to generate a voltage varying between 0 and 5 volts.
The output of the potentiometer is connected to one analog input pin of Arduino. This voltage is measured by a meter.
Write a program to read the output of the potentiometer. As pot output is varied from 0 to 5 volts, the value read varies from 0 to 1023.
Next the digital value is converted to analog by using the equation. Both values are displayed on monitor. The analog value should match that of meter

## Slide 86: Circuit and program

## Slide 87: Program
int Vi;
float Vo;
void setup()
{
Serial.begin(9600);
}
void loop()
{
Vi = analogRead(A1);
Vo = (5.0/1023.0)*Vi;
Serial.println(“Digital Value");
Serial.println(Vi);
Serial.println();
Serial.println(“Analog Value");
Serial.println(Vo);
Serial.println();
delay(2000);
}

## Slide 88: analogWrite function
Certain digital pins can be used as PWM pins
analogWrite( pin number, value);
value is an integer from 0 to 255
Decides the duty cycle of the PWM waveform
value 0 means 0% duty cycle
255 means 100% duty cycle

## Slide 89: PWM waveform
Tw
T
t
v
5

## Slide 90: Average value
analogWrite( pin number, value);

## Slide 91: Value and average value
Value | Average Value
0 | 0
25 | 0.490196078
50 | 0.980392157
75 | 1.470588235
100 | 1.960784314
125 | 2.450980392
150 | 2.941176471
175 | 3.431372549
200 | 3.921568627
225 | 4.411764706
255 | 5
Chart: Value
| 0 | 25 | 50 | 75 | 100 | 125 | 150 | 175 | 200 | 225 | 255
Average Value | 0 | 0.4902 | 0.98039 | 1.4706 | 1.9608 | 2.451 | 2.9412 | 3.4314 | 3.9216 | 4.4118 | 5

## Slide 92: Average calculation
analogWrite( pin number, value);
Examples

## Slide 93: Class Exercise 4.3
This exercise will demonstrate how the average value from a PWM output can be extracted by using a low pass first order filter
Use pin no 11 as output pin. Connect the output of pin no 11 to the R-C low pass filter
Use pin no 2 as the digital input pin. And use a slide switch which will enable you to connect either +5 or Ground to the input pin no 2.
Write a program to generate two different average values from pin no 11 for two settings of the slide switch.

## Slide 94: Interface circuit
From Digital pin 2
+5 volts
Ground
Time constant 20 mS

## Slide 95: Connections

## Slide 96: Program
bool x;
void setup()
{
pinMode(11, OUTPUT);
}
void loop()
{
x = digitalRead(2);
if (x == 1)
{
analogWrite(11,127);
}
else
{
analogWrite(11, 31);
}
}

## Slide 97: Control systems
Ashok Ranade

## Slide 98: Control system
What is a control system ?
It is a system which controls a physical quantity such as temperature or position
An example
Toaster
Function is to bring the bread slices to a desired
temperature so that they are nice golden brown.
Set the timer and put the supply on.
Next : Parts of a control system

## Slide 99: Parts of a control system
Control element
Timer
Plant
Heating coil
Control element
Regulator
Plant
Motor
Next : Open loop control system

## Slide 100: Open loop control systems
The control action is independent of the controlled
variable
Timer setting is assumed to be correct
But it may have to be different in winter compared
to summer
Also plant characteristics might change due to ageing
Controller
Plant
Reference input
Controlled variable
Next : Closed Loop control system

## Slide 101: Closed loop control system
Manual control
User adjusts a small time on timer
The user inspects the slices at the end of time
If not done he/she sets the time again and repeats
until done
Control action now depends on the output variable
Feedback is used in automatic control systems
Next : Speed control of DC motor

## Slide 102: Speed control of a DC Motor
Variable DC voltage
DC Motor
Speed is proportional to DC voltage.
Input DC source can be calibrated in terms of speed.
The knob is set to the desired speed
Speed might change due to change in the load or ageing

## Slide 103: Manual Control
Variable DC voltage
DC Motor
Speed Sensor
Meter

## Slide 104: Automatic control
DC Motor
Speed Sensor
Meter
+
-
Vs
A
Vf
Sensor Characteristics | 
Speed | Vf
1000 rpm | 1 volt
2000 rpm | 2 volt

## Slide 105: Steady state calculation
DC Motor
Speed Sensor
Meter
+
-
Vs
A
Vf
Ks = Vf/N

## Slide 106: Exercise 5.1
A dc motor has linear characteristics between input voltage and speed. Two points on this characteristics are
N = 600 rpm when V = 15 volts
N = 800 rpm when V = 20 volts
(1) Find the equation between speed and the
voltage.
(2) when loaded the proportionality constant between
speed and voltage becomes 1/3 of the no load
value. Find the new speed at V = 15 volts and find
the % change in the speed compared to no load

## Slide 107: Solution

## Slide 108: Exercise 5.2
DC Motor
Speed Sensor
Meter
+
-
Vs
A
Vf
Consider the above closed loop system.
Km = 40 and Ks = 1/160. Find the speed of the motor when
Vs = 5 volts and A = 10
the motor is loaded and Km drops to 40/3
Also find % change in speed

## Slide 109: Solution to Exercise 5.2

## Slide 110: Exercise 5.3
Repeat Exercise 5.2 but with A = 100.

## Slide 111: Answers
With A =100 | 
On No load | 
Vf | 4.807692
N | 769.2308
With load | 
Vf | 4.464286
N | 714.2857
% Change | -7.14286

## Slide 112: Specification of control systems
Accuracy of the output in steady state
Suppose desired temperature is 50 degrees
In a certain system the output could be within 1 %
Speed of response
How fast the desired output is achieved ?
One system : 5 minutes
Another system : 10 minutes
Feedback will help improve both
Next : An example of modelling

## Slide 113: Steps in analysis of control systems
From the block diagram set up the differential equation for the system
Solve the differential equation
Find the steady state error
Find the speed of response
The differential equation can be
First order
Second order or higher order

## Slide 114: Block diagram of an oven
Heating Element
Thermo Couple
Next : Thermal resistance

## Slide 115: Thermal resistance and capacitance
When the power is supplied the temperature in the oven increases
The rate of increase depends on thermal resistance and thermal capacitance
Thermal resistance
This impedes the heat flow(Energy/unit time) from
oven to outside
Depends on the materials and geometry
Note R is in degrees/Watt

## Slide 116: Thermal capacitance
Consider an oven with no leakage
The temperature in the oven will start with ambient temperature and increase as the heat energy in creases with time. Thus the heat energy is being stored.
Larger the volume , smaller will be the rate of increase of temperature
C is in watt-sec/degree

## Slide 117: Mathematical model of the oven
Heat in = Heat out + Heat Stored
Next : An example of steady state calculations

## Slide 118: Steady state calculations
In steady state , the temperature in the oven becomes constant and the equation is
A sample calculation
Suppose we want and .
Also R = 0.05 Degrees/ Watt
Coil wattage q = 40/0.05 = 800 watts

## Slide 119: Electrical Equivalent circuit
Temperature : Voltage
Thermal resistance : Electrical resistance
Thermal capacitance : Electrical capacitance

## Slide 120: Set point
Note that q reaches qR in steady state. This the desired temperature. Hence qR is called the set point
In the electrical Analog V is the set point
Next : Closed loop system

## Slide 121: Closed Loop System

## Slide 122: Effect of proportional control
Time constant is reduced. Faster Response
Steady state error

## Slide 123: Loading effect in Open loop System
Steady state voltage is reduced to half the value.

## Slide 124: Loaded system with feedback

## Slide 125: LTspice simulation

## Slide 126: Step response

## Slide 127: Exercise 5.4
In the Ltspice simulation shown the load is the first order low pass filter consisting of 1kohms resistor, 1000 mF capacitor and the load of 1 kohms resistor
Replace this load by a second order low pass filter consisting of 20 kohms resistor, 0.1 H inductor and 1mF capacitor. Use a load of 40 kohms resistor and plot the transient response for open loop and closed loop circuit and compare.
Write your conclusions.

## Slide 128: Solution to Exercise 5.4

## Slide 129: Open loop and closed loop outputs

## Slide 130: Sensors, Instruments and Experimentation
By Ashok Ranade
07 Concepts of Stress
and Strain

## Slide 131: Hook’s Law
When you apply a Force to an object, it moves if free to move
If it is not free to move, it gets deformed.
Hook’s law (Applies when deformation is small)
F is the force applied
k constant depending on shape and composition of
the object and the direction of the force
The amount of deformation

## Slide 132: Deformation vs Force

## Slide 133: Axial and transverse strain Tensile force
F
F
Typically
Lies between 0 to 0.5

## Slide 134: Compressive Force
F
F

## Slide 135: Young’s modulus
F
F
A : Cross sectional area
Y : Young’s Modulus
Stress = Y x Strain

## Slide 136: Young’s modulus for various materials

## Slide 137: Exercise 7.1
A sculpture weighing 10,000 N rests on a horizontal surface at the top of a 6.0-m-tall vertical pillar. The pillar’s cross-sectional area is 0.20 m2 and it is made of granite with a mass density of 2700 kg/m3 . Find the compressive stress at the cross-section located 3.0 m below the top of the pillar and the value of the compressive strain of the top 3.0-m segment of the pillar.

## Slide 138: Solution
The volume of the pillar segment with height h = 3.0 m and cross-sectional area A = 0.20 m2 is
V = Ah = 0.6 m3
With the density of granite = 2.7 x 103kg/m3 , the mass of the pillar segment is
m = ρV = 1.6x103 Kg
The weight of the pillar segment is
w = mg=1.568x104 N

## Slide 139: Solution continued
The weight of the sculpture is w = 1.0 x 104 N
So the normal force acting
wp+ws = 2.568x104 N
Stress = F/A = 2.568x104/0.2 = = 128.4 kPa
Y for granite= 4.5x107 kPa
Strain = Stress/Y= 2.85x10-6
Note that the stress will be maximum at base

## Slide 140: Exercise 7.2
A 2.0-m-long steel rod has a cross-sectional area of 0.30cm2 The rod is a part of a vertical support that holds a heavy 550-kg platform that hangs attached to the rod’s lower end. Ignoring the weight of the rod, what is the tensile stress in the rod and the elongation of the rod under the stress?

## Slide 141: Answers
Procedure
Calculate F/A
Young’s modulus for steel is Y =2.0×1011Pa.
Calculate DL

## Slide 142: Strain gauge
Tension will increase the resistance
Special plastic
Epoxy adhesives

## Slide 143: Strain gauge
Compression will decrease the resistance
Special plastic
Epoxy adhesives

## Slide 144: Various gage factors

## Slide 145: Simple method of strain measurement
Strain gage
Voltage across the strain gauge is
Voltage can be calibrated in terms of strain. But measurement will be very difficult since DR/R is very small compared to one.

## Slide 146: Bridge circuit

## Slide 147: Quarter Bridge Configuration 1
Axial or bending strain

## Slide 148: Quarter bridge Configuration 1

## Slide 149: Calculation for strain

## Slide 150: Exercise 7.3
Assume a quarter bridge driven by a 9 volt battery
Gauge factor has the value of 3
Next assume that a variable tensile force is applied
This force is adjusted to get the output voltage from 0 to – 130 mvolts in steps of -10 mVolts
Using a spreadsheet calculate the strain values for each of the output observed

## Slide 151: Answers
Vo | Strain(%)
0 | 0
-10 | 0.148478099
-20 | 0.297619048
-30 | 0.447427293
-40 | 0.597907324
-50 | 0.74906367
-60 | 0.900900901
-70 | 1.053423627
-80 | 1.206636501
-90 | 1.360544218
-100 | 1.515151515
-110 | 1.670463174
-120 | 1.826484018
-130 | 1.983218917

## Slide 152: Exercise 7.4
Next set up a quarter bridge circuit in Tinkercad to measure the output voltage from the bridge. Use 100 ohms bridge resistors and a 9 volt battery.
Since Tinkercad does not have strain gage use a variable resistance varying from 0 to 6 ohms to represent the strain gauge.
Use an identical resistance in the other arm to compensate for a possible offset.
Vary the resistance and record the output voltage

## Slide 153: Exercise 7.3 continued
What is the value of output voltage you expect when the resistance is set to 6 ohms? Explain your answer.

## Slide 154: Solution

## Slide 155: Solution continued
From the table in the spreadsheet we expect the output of about -130 mV. We get -129 mV

## Slide 156: Quarter Bridge configuration 2
R3 is mounted in close thermal contact
but not bonded to the specimen.
So strain does not affect R3 but temperature
Effects are cancelled since ratio of R3 to R4
becomes independent of temperature
Axial or Bending strain

## Slide 157: Half bridge Strain gage Axial or bending strain
R3 is mounted in close thermal contact
and bonded to the specimen.
Temp effects are cancelled since ratio of R3 to R4
becomes independent of temperature
v is the Poisson ratio

## Slide 158: Full Bridge (Bending strain only)

## Slide 159: Full Bridge (Axial strain)

## Slide 160: Sensors, Instruments and Experimentation
By Ashok Ranade
17 Force sensing Resistance

## Slide 161: Principles of Force sense resistor
Conducting foam. Polyethylene foam filled with carbon.
When pressed the contact resistance will decrease.

## Slide 162: Foam used as resistor

## Slide 163: Resistance change detected

## Slide 164: Conducting grid
A polyester film with printed circuit
Conducting fingers

## Slide 165: Two types of FSR
Conducting sheet is polymer sheet with carbon ink
Thru mode more sensitive to light forces and more linear. Costlier

## Slide 166: Tinkercad simulation

## Slide 167: Force vs Resistance characteristics
F(Newtons) | R(Kohms)
0.1 | 64.2
0.18 | 33.2
0.32 | 16.5
0.39 | 13.3
0.88 | 6.58
1.76 | 4.03
3.09 | 2.72
4.81 | 2
6.76 | 1.58
8.48 | 1.34
10 | 1.2
Chart: 
| 0.1 | 0.18 | 0.32 | 0.39 | 0.88 | 1.76 | 3.09 | 4.81 | 6.76 | 8.48 | 10
R(Kohms) | 64.2 | 33.2 | 16.5 | 13.3 | 6.58 | 4.03 | 2.72 | 2 | 1.58 | 1.34 | 1.2

## Slide 168: Force vs voltage

## Slide 169: Tinkercad simulation

## Slide 170: Force vs output voltage
F(Newtons) | R(Kohms) | Vo = 12*(1/(1+R)
0.1 | 64.2 | 0.18404908
0.18 | 33.2 | 0.350877193
0.32 | 16.5 | 0.685714286
0.39 | 13.3 | 0.839160839
0.88 | 6.58 | 1.583113456
1.76 | 4.03 | 2.385685885
3.09 | 2.72 | 3.225806452
4.81 | 2 | 4
6.76 | 1.58 | 4.651162791
8.48 | 1.34 | 5.128205128
10 | 1.2 | 5.454545455
Chart: 
| 0.1 | 0.18 | 0.32 | 0.39 | 0.88 | 1.76 | 3.09 | 4.81 | 6.76 | 8.48 | 10
Vo = 12*(1/(1+R) | 0.18405 | 0.35088 | 0.68571 | 0.83916 | 1.5831 | 2.3857 | 3.2258 | 4 | 4.6512 | 5.1282 | 5.4545

## Slide 171: Force alarm
In this circuit if Force exceeds a certain value an alarm is given in the form of lighting the LED
Vref= 4 volts
4.81 Newtons

## Slide 172: Tinkercad Simulation

## Slide 173: Exercise
Design and build a force-meter
Use the suggested circuit for sensing the force
Use an analog pin to read the input
Use curve-fitting to convert the input into force in Newtons.

## Slide 174: Solution
A crude solution is given in the next few slides.
The calibration is good only for larger values of Force
Students are expected to do better curve fitting

## Slide 175: Force-meter circuit

## Slide 176: Program
float(F);
float(V);
void setup()
{
Serial.begin(9600);
}
void loop()
{
V = analogRead(1);
if (V < 145)
{
F = 0.000018* V*V + 0.0042122*V;
}
else if(V >= 145 && V <= 260)
{
F = 0.0000417*V*V+0.0013314*V +0.30588 ;
}
else
{
F = 0.0000832*V*V-0.0256711*V+3.8517;
}
Serial.println(F);
}

## Slide 177: Output

## Slide 178: Sensors, Instruments and Experimentation
By Ashok Ranade
14 Potentiometer
as position transducer

## Slide 179: Potentiometer

## Slide 180: Potentiometer constant

## Slide 181: Converting change of resistance into a change of voltage

## Slide 182: Application in an automobile
When accelerator pedal is pressed in an automobile throttle valve opens wider allowing more air to go in the engine providing larger energy.
Precise control of throttle valve can be obtained by using feedback
Two potentiometers are used. One to sense the pedal position and the other to sense throttle valve position.

## Slide 183: Feedback control
Motor
Throttle valve and sensor
+
-
From Pedal pot
Pulse
Width
Modulator

## Slide 184: Pulse width modulation
More efficient than using a DC amplifier

## Slide 185: Throttle valve

## Slide 186: Throttle valve angle and Potentiometer output
At 0 degrees the throttle valve is closed. At 90 degrees it is fully open.

## Slide 187: Pedal angle and Potentiometer output
At 0 degrees the accelerator is
un-pressed. At 45 degrees it is fully pressed.

## Slide 188: Angle measurement using arduino Exercise 9.1
Interface a potentiometer to Arduino in Tinkercad using analog input pin.
Note that potentiometer goes from zero degrees to 270 degrees.
Write the program to read the input from the potentiometer and display the angle on serial monitor

## Slide 189: Angle measurement

## Slide 190: DC motor control using Arduino
A dc motor is interfaced to Arduino
The speed of the dc motor will depend on the applied voltage
Direction of the rotation will depend on the direction of current through the winding.
Direction of rotation can be reversed using a H bridge

## Slide 191: H bridge
S2, S3 open
S1, S4 closed
Current flows from left to right
S2,S3 closed
S1, S4 open
Current flows from right to left reversing the direction of rotation

## Slide 192: H Bridge IC
This can control two motors
Vcc1 should be +5 volts. This is used for logic circuits.
Voltage to Vcc2 is for the motor. This can have values from 4.5 volts to 36 volts.
Out1 and Out2 go to motor terminals.
IN1 and IN2 control direction of rotation as follows
When ENA is high the motor runs. When it is low the motor stops. So if a PWM waveform is connected to ENA speed can be controlled through duty cycle
Similar controls for the second motor

## Slide 193: Exercise 9.2
Design the hardware and software interface to arduino for direction and speed control of a dc motor. (Use hobby gear-motor in Tinkercad)
Use a potentiometer and an analog input pin to provide a variable voltage to the Arduino. In the program scale this so as to generate a PWM signal of variable duty cycle to be connected to Enable pin.
Use a slide switch to generate a digital input. If this is high motor should run in one direction. Otherwise in the opposite direction.

## Slide 194: Hardware interface

## Slide 195
float x; float y;
void setup()
{
pinMode(11, OUTPUT);
pinMode(4, OUTPUT);
pinMode(2, OUTPUT);
}
void loop()
{
if (digitalRead(7) == HIGH)
{
digitalWrite(4,HIGH);
digitalWrite(2,LOW);
}
else
{
digitalWrite(4,LOW);
digitalWrite(2,HIGH);
}
x = analogRead(A1);
y = x*255/1023 ;
analogWrite(11,y);
}

## Slide 196: Sensors, Instruments and Experimentation
By Ashok Ranade
10 Temperature
Detectors

## Slide 197: Resistance temperature detectors (RTD)
RTD is a resistance which depends on temperature
RTDs can be made with both positive and negative temperature coefficients.
To develop a voltage proportional to temperature a current source is required

## Slide 198: Platinum RTDs
Platinum has high resistivity
1.06×10−7 ohm-meter at 200C
RT = [Ro + (αRoΔT)]
= 0.00385 Ω/Ω/°C at 0°C
A typical value R0 = 100 ohms

## Slide 199: Approximate relationship
Chart: 
| 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800
RTD | 100 | 138.5 | 177 | 215.5 | 254 | 292.5 | 331 | 369.5 | 408
T | 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800
RTD | 100 | 138.5 | 177 | 215.5 | 254 | 292.5 | 331 | 369.5 | 408
Temp in 0C
Resistance in ohms

## Slide 200: Temperature calculation
RTD
T

## Slide 201: Line resistance effect
Voltmeter
Current source
RTD
Heated chamber
Monitoring place
If the distance between monitoring place and the chamber is large line resistances will cause error
Calibrated in temperature

## Slide 202: 4-Wire RTD measurement
Voltmeter
Current source
RTD
Heated chamber
Monitoring place
Voltmeter has large resistance so very little current flows through measurement wires
Calibrated in temperature

## Slide 203: Resistance as a function of temperature
A better approximation is
R = R0(1 + AT – BT2 - CT3)
A = 3.6962x10-3 : B = 5.8494x10-7
C = 4.2325x10-12

## Slide 204: Thermocouples
Thermocouple is basically a junction of two dissimilar metals and gives a voltage depending on the temperature of the junction
Discovered by Thomas Seebeck in 1821

## Slide 205: Types
The first metal has +ve polarity

## Slide 206: Merits and demerits
Much higher temperature range compared to RTD
Much more rugged
Non-linear characteristics
Less accurate.

## Slide 207: Reference(Cold) junction
There is one hot junction and two cold junctions. The output voltage is the resultant of all the voltages produced. But if the reference junctions are kept at zero degree centigrade their voltages are zero and the output voltage corresponds to the temperature of hot junction.

## Slide 208: Calibration

## Slide 209: Polynomial for J thermocouple
T = -0.048868252 + 19873.14503 v - 128614.5353 v2 + 11569199.78 v3 - 264917531.4 v4 + 2018441314 v5

## Slide 210: Polynomial for J thermocouple
v | 0 | 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06
T | -0.05 | 194.9 | 402.6 | 627.2 | 858 | 1093 | 1364
Chart: 
| 0 | 0.01 | 0.02 | 0.030000000000000002 | 0.04 | 0.049999999999999996 | 0.05999999999999999
T | -0.048868 | 194.943 | 402.594 | 627.2257 | 858.022 | 1093.2504 | 1364.4834
V in volts
T in degrees C

## Slide 211: Reference junction compensation
VH
+
_
+ VC1 -
+ VC2 -
+
-
The temperature of the reference junction is regulated at some convenient value. Hence VC1 and VC2 are known .V is measured. Note that polarities shown are assumed polarities. They could be different for different type of junctions.
VH = VC1 + V – VC2
From the characteristics of the thermocouple T1 can be calculated

## Slide 212: Automatic junction compensation
Processor
Cold J unction Temp
Measurement
Integrated circuit or
RTD circuit
VT
+
-
+ V1 -
+ V2 -
+
Vout
-
Algorithm
Read Vout through an ADC
Read cold junction temperature
Calculate V1 and V2
Calculate
VT = V1 + Vout –V2
(5) Calculate the hot junction
temperature
(6) Display temperature
(7) Delay
(8) Go to (1)
The polarities of VT, V1 and V2 depend on the metals
44.90C
Display

## Slide 213: Temperature sensor TMP 36
Low voltage operation (2.7 V to 5.5 V)
Calibrated directly in °C
10 mV/°C scale factor (20 mV/°C on TMP37)
±2°C accuracy over temperature (typ)
±0.5°C linearity (typ)
Stable with large capacitive loads
Specified −40°C to +125°C, operation to +150°C
Less than 50 μA quiescent current
Shutdown current 0.5 μA max
Low self-heating
Qualified for automotive applications
When Temp = -400C Vo = 100 mV
When Temp = 1250C Vo = 1750 mV

## Slide 214: Exercise 10.1
Interface the IC TMP 36 to arduino in Tinkercad
IC has three terminals. Vcc, Ground and Vout
Use an analog pin to read the output of TMP 36
Perform necessary calculation to obtain the temperature
Display the temperature on the serial monitor
Note that you will see a slider on top of the IC once the simulation has started. This can be used to change the temperature.
In actual application the temperature is decided by the surroundings

## Slide 215: Calculation required
The value read (say, Vd) by the analogRead command will be the digital value ranging from 0 to 1023. And it will be 1023 when the input voltage is 5 volts. So the realtion between Vd and Vo is given by

## Slide 216: Solution (Minimum Temperature)

## Slide 217: Highest temperature